## Slide 1
Operation and Troubleshooting of Lagoons
Presented by

## Slide 3
Pre Test

## Slide 4: What are Lagoons?
Ponding of wastewater to:
  Stabilize the waste
  Cause die-away of pathogens
  Allow percolation, evaporation or controlled discharge, and land application
Stabilize: waste that has been treated or decomposed to the extent that if discharged or released, its rate and state of decomposition would be such that the waste would not cause a nuisance or odor.

## Slide 5: Why use Lagoons?
Advantages:
  Reduced O&M
  Operator Certification Level
  Effluent limits
  No Discharge Possible (complete retention)
  Meet Fecal Limits
  Sludge disposal
  Changes in Temperature
  Load Fluctuations

## Slide 6: Why Use Lagoons
Disadvantages:
  Rely on Light as Energy Source
  Space (requires large areas for retention and treatment.
  Banks subject to wind and animal erosion
  Sludge can be more difficult to get rid of

## Slide 7: Operation and Troubleshooting of Lagoons
EPA Classifications: I, 2 and 3
Types: Aerobic, Anaerobic, Facultative
Types: Primary, Secondary, Tertiary
Design Parameters
Size & Depth
Biological Processes
Chemical Enhancements?

## Slide 10: Most Lagoons are “Facultative”: - 4 to 8 ft deep - both aerobic & anaerobic digestion

## Slide 11: Aerated Lagoons

## Slide 12: Anaerobic Lagoons (without Oxygen)
Deep lagoon (> 8 ft. deep)
No dissolved oxygen
Not aerated, heated or mixed
Typically for pre-treatment and sedimentation of suspended solids
Can have odor problems
Long retention times, especially in cold climate (un-effective below 27 F)

## Slide 13: Other Lagoons: Fun Type

## Slide 14: Lagoon operations
Health & Safety
Sampling & Monitoring (when?)
Controlling Flows & Levels
Chemical Addition?
Trouble Shooting Problems

## Slide 15: Lagoon Maintenance
Inspections: Observations & Records
EPA Permit requirements
Sludge/Grit control & removal
Maintaining Dikes
Plant & Critter control
Mechanical systems
Schedule

## Slide 16: Typical Lagoon

## Slide 17: Good Signage

## Slide 18: WW Lagoon Problems
Sign old or unreadable
Gates or sign or locks missing
Fences down or cut
Over grazing or erosion from livestock
Dry lagoons (size or flow issues)
Burrows
Inflow or Drain plugged
Cattails and/or trees

## Slide 19: Old Sign

## Slide 20: Plant Growth

## Slide 21: Trees & Brush

## Slide 22: Overgrown Lagoon - Low Flow

## Slide 23: Over Grazing

## Slide 24: Lagoon Guard

## Slide 25: Erosion from Cattle

## Slide 26: Fences Down

## Slide 27: Wave Erosion

## Slide 28: Critter Burrows

## Slide 29: Inflow Blockage?

## Slide 30: Security

## Slide 31: Flow: pond to pond

## Slide 32: Blockage

## Slide 33: Outflow

## Slide 34: Debris in Lagoon

## Slide 35: Piping

## Slide 37: Observations and Record Keeping
Wastewater
  Color, Scum, Weeds, Algae, Odors, Ice
Dikes (Berm)
  Weeds, Holes, Erosion
Pond Structures
  Blockage, Grease, Corrosion, Erosion, Valves
Aeration System
  Operation, Patterns, Valves

## Slide 38: Questions?
Contact information:
Gregg Hinrichsen
Midwest Assistance Program
308 – 528 - 1048
ghinrichsen@map-inc.org