## Slide 1: RECORD KEEPING Spring 2021
Gregg Stewart
North Dakota Department of Environmental Quality
701-328-6621
gstewart@nd.gov

## Slide 2: WHY KEEP RECORDS?
Required by law
Track routine maintenance
Track treatment problems/optimize treatment

## Slide 3
Provide basis for annual reports
Help control the quality of the water being discharged
Provide a basis for possible financial aid

## Slide 4
Protect yourself/system from unnecessary litigation/unjust claims
- i.e. odor problems, sewer backups, permit violations, work related accidents, etc.

## Slide 5: WHERE TO KEEP RECORDS?
Two separate locations is ideal
- Operator has one copy
- City auditor (or other designated city official has the other copy)
NOTE: Monitoring records must be kept on file for at least 3 years

## Slide 6: EXAMPLES OF RECORDS THAT SHOULD BE KEPT
Date, place and time of any samples collected
Individual who took the sample(s)
Date(s) analyses were performed

## Slide 7
Individual who performed analysis and method used
Results of analyses (pH, BOD, total suspended solids, fecal coliforms, ammonia, chlorine, metals, whole effluent toxicity, hydrogen sulfide, oil/grease, dissolved oxygen)

## Slide 8
Preventive maintenance records (for each piece of equipment)
Preventive maintenance schedule (i.e., when valves are exercised)
Service report cards

## Slide 9
Spare parts inventory
List of where spare parts can be purchased
Operation and maintenance manuals

## Slide 10
Specifications on equipment from suppliers
Equipment inventory
Lift station pump hours (must keep hour meter readings/kilowatt hour usage)

## Slide 11
North Dakota Pollutant Discharge Elimination System (NDPDES) permit
Discharge approvals
-also when discharge started and ended

## Slide 12
How flow is determined while discharging (no more than 6 inches per day in order to minimize release of bottom solids)
Discharge Monitor Report (DMR) forms
  Include amount of water discharged within 10%
  Submitted to Dept. of Environmental Quality every 6 months

## Slide 13
Operation manuals/manufacturers literature
Design Engineers Report and Specifications
Budgets/maintenance costs

## Slide 14: Do your wastewater ponds hold water or are they seeping? Or is your discharge pipe leaking?

## Slide 15: When was the last time you checked your discharge pipe? (must be screened or have a flapper valve) If it is leaking, must test if water is wastewater or groundwater

## Slide 16: Sample must be collected and analyzed for: fecal coliform, BOD, TSS, pH, nutrient scan, and general chemistry If it is wastewater, valve must be repaired or replaced

## Slide 30: QUESTIONS? 1. Keeping adequate records is required by law. (T or F) 2. Monitoring records should be kept on file for at least ____ years.

## Slide 31
3. Keeping good records may protect a system from unjust litigation. (T or F)
4. Wastewater systems should keep track of when a discharge from a pond ______
and ______.

## Slide 32
5. When discharging a pond, the pond should be lowered no more than _________ per day.